## Slide 1: ITP05
Network Management
angelitoicunananjr@gmail.com
aicunananjr.weebly.com

## Slide 2: 700BC
#throwback
Notes: The Greeks used homing pigeons to establish rudimentary (basic principle) information network
homing pigeons find its way home over extremely long distances.

## Slide 3: 1819
Hans Oersted
Notes: Wire that carrying electric current could deflect (change direction) a magnetized needle
Opening the way for wire-based telegraph networks.

## Slide 4: What is a network?
Word-of-mouth communication, cell phone or telephone, & computer
Notes: Basic network - Word-of-mouth communication

## Slide 5: Cell phone or Telephone
As network
Notes: Cellphone – radio waves
Telephone – connected to miles of cables
All connected to world by vast network of communications equipment

## Slide 6: What is a Computer network?
A system of computers, print devices, network devices and computer software linked by radio waves or communication cable
Notes: Data over Copper wire before
Data, voice, video communications over wire, fiber-optics media,
radio waves, infrared waves, and microwaves today

## Slide 7: Types of Network
PAN, LAN, CAN, MAN, WAN

## Slide 8: PAN
Personal Area Network - very small distances and lowest in complexity
Notes: Roughly about 10 meters or 33 feet

## Slide 9: LAN
  Local Area Network - Interconnects computers, printers, other equipment that share hardware and software resources in close physical proximity

## Slide 10: MAN
  Metropolitan Area Network - Spans a greater distance than a LAN. Links same organization or to several different organizations
Notes:     Up to 48 kilometers (about 30 miles)
  Links multiple LANs within city or metropolitan region
  (Typically uses fiber-optic/wireless connections)

## Slide 11: CAN
  Campus Area Network – Similar to MAN, but the difference is that all of the LANs and the buildings housing the LANs are owned by one Organization.

## Slide 12: WAN
  Wide Area Network – Composed of two or more LANs, MANs, or CANs
Notes:   Connected across a distance greater than 48 km (30 miles)

## Slide 13: Basic Networking Terms

## Slide 14: Node
  - AKA (station): any device connected to a network
  3 nodes important to users:
    Workstations
    Hosts
    Servers
Notes:   Personal computer, server, mainframe, supercomputer,
  printer, fax, DVD/CD-ROM, disk array, network device

## Slide 15: 3 nodes important to users:
    Workstations – has CPU, OS, Applications like MS Office, & may fulfil roles as client (workstation accessing data or software on another computer) and host
    Hosts - the computer accessed for data or software by a client workstation
    Servers - Powerful computers offering multiuser access
Notes:   1. Personal computer, server, mainframe, supercomputer,
  printer, fax, DVD/CD-ROM, disk array, network device
  2.
  3. Holds software applications and data files
  Users who visit a website are accessing a server

## Slide 16: 3 nodes important to users:
    Workstations – has CPU, OS, Applications like MS Office, & may fulfil roles as client (workstation accessing data or software on another computer) and host
    Hosts - the computer accessed for data or software by a client workstation
    Servers - Powerful computers offering multiuser access
Notes:   1. Personal computer, server, mainframe, supercomputer,
  printer, fax, DVD/CD-ROM, disk array, network device
  2.
  3. Holds software applications and data files
  Users who visit a website are accessing a server

## Slide 17: 3 nodes important to users:
    Workstations – has CPU, OS, Applications like MS Office, & may fulfil roles as client (workstation accessing data or software on another computer) and host
    Hosts - the computer accessed for data or software by a client workstation
    Servers - Powerful computers offering multiuser access
Notes:   1. Personal computer, server, mainframe, supercomputer,
  printer, fax, DVD/CD-ROM, disk array, network device
  2.
  3. Holds software applications and data files
  Users who visit a website are accessing a server

## Slide 18: Using network in a Home…
Notes:   Sharing files and printers
  Accessing the Internet and entertainment resources
  Connecting home resources (Computers, entertainment devices, appliances)
  ICS – Internet connection Sharing: network and sharing center> Change adapter>properties of specific network.

## Slide 19: Using network in an Office…

## Slide 20: Business Strategy
Notes:   Using internet connections (simple order system)

## Slide 21: 4 Network Properties
    Communication Medium
    Protocol
    Topology
    Network type (private vs. public)
Notes:   Changing of a one medium to another. Fiber>waves… etc.
  How each unit is transmitted and how it is being interpret (chapter 2)
  The design layout: 2 components
    Physical Layout
    Logical Path
  From private (local) to public (internet): the boundaries starts at the point when local meets public

## Slide 22: Network Topologies
Is a physical layout combined with logical path.
  Decentralized network layout - Cable running between each station on network
  Centralized network layout - Each station physically connected to central device
Notes:   1. Physical layout – which the cabling is laid in the building, office etc. is also often called cable plant

## Slide 23: 1. Bus topology
  Has starting point and an end
  Point (terminator).
  Like a chain
Notes:   When transmitting a packet across a bus:
  It is detected by all nodes on the segment
  Given time limit to reach destination or it is considered late

## Slide 24
Notes:   Example of connectors in bus topology and
  Tp/ft-10 BUSterminator

## Slide 25: IEEE - Institute of Electrical and Electronics Engineers
International organization of scientist, engineers, technicians, and educators
Notes:   Develops standards for network cabling, transmission
Advantages of bus design
  Requires less cable than other topologies
  Easy to extend bus with a workstation
Disadvantages of bus topology
  High management costs
    Single defective node can take down entire network
  Can become quickly congested with network traffic

## Slide 26: 2. Ring topology
Advantages to ring topology
  Easier to manage than bus
  Suited to transmitting signals over long distances
Disadvantages to ring topology
  More expensive to implement than bus
  Has become outdated so there are fewer equipment options
Notes:   Continuous data path with no beginning or ending point
  Before: one loop (cycle) then back to source
  Now: Two loops for redundant data (for assuring the transfer of data) > opposite direction

## Slide 27
Notes:   Before: one loop (cycle) then back to source
  Now: Two loops for redundant data (for assuring the transfer of data) > opposite direction

## Slide 28: 3. Star topology
Advantages
  Start-up costs are much lower than other topologies
  Easier to manage, defective nodes quickly isolated
  Easier to expand by connecting nodes or networks
  Offers better equipment and high-speed options
  Cabling and connectors are less expensive
Disadvantages
  Failure of central device may cause network failure
  Requires more cable than bus
Notes:   The oldest communication design method
  multiple nodes attached to central device (hub, switch, router)

## Slide 30: 4. Star-Bus Hybrid topology
Advantages of star-bus topology
  No exposed terminators
  Easily connect switches/routers to expand network
  Connection between central devices is a backbone
    Backbone enables high-speed communication
  Central devices have built-in intelligence to help detect problems
  Many equipment and high-speed options available
Notes: Star-Wired Bus Topology
  Each radiating finger is separate logical bus segment,
  Each segment terminated at both ends

## Slide 32: 5. Star-Ring Hybrid topology
  Hub or access unit acts as linking device
  Transmission of signal uses logical communication of ring
  No need for built-in terminators

## Slide 34: 6. Mesh topology
Every node is connected to every other node in network
Provides fault tolerance
  Expensive to implement
Notes: Fault tolerance: built-in protection against failure
If link breaks, nodes can still communicate

## Slide 36: 6. Tree topology
Advantage of the tree topology:
  Can segregate network traffic so that communications in one limb of the tree can be isolated from other limbs
    Important for highly secure networks
Disadvantage of the tree topology:
  On cabled networks, may require more cable
  If main trunk is down, connected limbs can not communicate with one another
Notes: expanded star
Consists of a trunk (or bus) with limbs and branches (star)

## Slide 37: Thank YOU!
End of slides…
Notes: p.36